## Slide 1: Obtekanie a odpor telies
prof. Ing. Dušan Kudelas, PhD

## Slide 2: Telesá a sily
Drag = pressure + friction
Odpor = tlakový + trecí
Fluid dynamic forces are comprised of pressure and friction effects.
Often useful to decompose,
  FD = FD,friction + FD,pressure
  CD = CD,friction + CD,pressure
This forms the basis of ship model testing where it is assumed that
  CD,pressure = f(Fr)
  CD,friction = f(Re)

## Slide 3: Telesá s dominantným trecím odporom

## Slide 4
DRAG COEFFICIENT - CD
CD = FD / (1/2 U2A)
Flow over a flat plate: FD = plate surface wdA
CD = PSwdA / (1/2 U2A)
Cf = w/(1/2 U2)
{Cf = shear stress or skin friction coef.}
CD = (1/A)PSCf dA
(good for laminar and turbulent flow)

## Slide 5
Flow over a flat plate with zero pressure gradient:
CD = (1/A) PS CfdA
Cf = 0.664/Re1/2 for laminar flow
(Blasius solution – flat plate laminar flow
& no pressure gradient)
CD = (1/A)A (0.664/Re1/2) dA
= (bL)-1 0L (0.664 U-1/2x-1/21/2) bdx
= (0.664/L) (/U)1/2 (2)x1/2oL = 1.33 ( / LU)1/2
CD = 1.33 (ReL) -1/2 for laminar flow over a flat plate,
with no pressure gradient

## Slide 6
Flow over a flat plate with zero pressure gradient:
CD = (1/A) PS CfdA
Cf = 0.0594/Re1/5 for turbulent flow
(u/U = [y/]1/7)
(Blasius correlation: f = 0.316/Re1/4; Re  105)
CD = (1/A)A (0.0594/Re0.2) dA
= (bL)-1 0L (0.0594 (U/)-0.2x-0.2 bdx
= (0.0594/L) (/U)0.2 [x0.8/0.8]oL
= 0.0742(/UL)0.2
CD = 0.0742 (ReL) –0.2 for turbulent flow over a flat
plate, with no pressure gradient - 5x105 <ReL<107

## Slide 7
CD = 1.33 (ReL) -1/2 for laminar flow over a flat plate, with no pressure gradient ~ Re < 5x105
CD = 0.0742 (ReL) –0.2* for turbulent flow over flat
plate, with no pressure gradient ~ 5x105 <ReL<107
CD = 0.455/ log (ReL)2.58* for turbulent flow over flat
plate, with no pressure gradient ~ ReL<109
* Assumes turbulent boundary layer begins at x=o

## Slide 8
CD correction term for
partly laminar / partly turbulent

## Slide 9
CD correction term for
partly laminar / partly turbulent
?
ADD
OR
SUBTRACT
CORRECTION
TERM ???

## Slide 10
Must account for fact that turbulence
does not start at x = 0
-must subtract B/ReL
CD correction term = B/ReL = Retr(CDturb – Cdlam)/ReL
Retr

## Slide 11
CD correction term = B/ReL = Retr(CDturb – CDlam)/ReL
For Retr = 5 x 105
CD = 0.0742/ReL1/5 – Retr(CDturb – CDlam)/ReL
CD = 0.0742/ReL1/5
– 5x105[0.0742/ (5x105)1/5–1.33/(5x105)1/2]/ReL
CD = 0.0742/ReL1/5 – 1748/ReL
Retr
5 x 105 < ReL < 107
Notes: Because Cdturb which is in B depends on Re range.

## Slide 12
CD correction term = B/ReL = Retr(CDturb – CDlam)/ReL
For Retr = 5 x 105
CD = 0.0742/ReL1/5 – Retr(CDturb – CDlam)
CD=0.0742/ReL1/5–5x105[0.455/ (log[5x105])1/5–1.33/(5x105)1/2]
CD = 0.455/(logReL)2.58 – 1600/ReL
Retr
5 x 105 < ReL < 109
Notes: Because Cdturb which is in B depends on Re range.

## Slide 13
SMOOTH FLAT PLATE
NO PRESSURE GRADIENT
CD = 0.0742 (ReL) –0.2
CD = 0.455/ log (ReL)2.58
CD = 1.33 (ReL) -1/2

## Slide 14
Rough Flat Plate

## Slide 15
FLAT PLATE
CD =
D/( ½ U2A)
ReL
Notes: Both flat plate and pipe do not have wakes.
Both have similar laminar and turbulent trends and function of roughness

## Slide 16
Telesá s dominantným tlakovým odporom

## Slide 17
Drag Force = p/t = (mv)/t
m ~ UAf = mass per second passing through area
v ~ U-0 = U
CD = D/(1/2 U2Af) ~ UAfU/(1/2U2Af)
CD ~ 2 Newton
Value is right order of magnitude,
& Re insensitivity predicted correctly.
(fixed)

## Slide 18
Mostly pressure drag, separation point fixed
Friction
drag
Character of CD vs Re curves for different shapes
press
& fric

## Slide 19
Obtekanie šikmej dosky

## Slide 20
Analytické riešenie
do 8°
od 8°

## Slide 21
Numerické riešenie sa realizovalo pre rýchlosti prúdenia 6 m/s a 20 m/s resp. (Re= 330 000, a 1120 000), modelmi turbulencie k-omega SST a SST transition.

## Slide 22
rýchlosti prúdenia 6 m/s a 20 m/s
Alfa = 5°
Alfa = 20°
Alfa = 45°

## Slide 23
rýchlosti prúdenia 2 m/s
distribúcia tlaku,
vektory prúdenia
tlakový koeficient
Modelovanie prúdenia vzduchu v okolí strechy budovy

## Slide 24
rýchlosti prúdenia 4 m/s
distribúcia tlaku,
vektory prúdenia
tlakový koeficient
Modelovanie prúdenia vzduchu v okolí strechy budovy

## Slide 25
rýchlosti prúdenia 6 m/s
distribúcia tlaku,
vektory prúdenia
tlakový koeficient
Modelovanie prúdenia vzduchu v okolí strechy budovy

## Slide 26
rýchlosti prúdenia 20 m/s
distribúcia tlaku,
vektory prúdenia
tlakový koeficient
Modelovanie prúdenia vzduchu v okolí strechy budovy

## Slide 27
Prúdenie pri rôznych uhloch sklonu strechy

## Slide 28
cp pri rôznych uhloch sklonu strechy,
1) H/B =0,5
2) H/B = 1
3) H/B = 1,5

## Slide 29
Flow parallel to plate –
viscous forces important and Re dependence
Flow perpendicular to plate –
pressure forces important and no strong Re dependence
What about Re dependence
for flow around sphere?
Re
CD
?

## Slide 30
Drag Coefficient, CD, as a function of Re for a Smooth Sphere
SMOOTH SPHERE

## Slide 31
Drag Coefficient, CD, as a function of Re for a Smooth Sphere
SMOOTH SPHERE
FD = 3VD
CD = ?

## Slide 32
CD = FD/(½ U2R2)
= 6UR/(½ U2R2)
= 24/Re
Laminar boundary layer
Turbulent flow in wake
Separation point moving forward
Separation point fixed
95% of drag due to pressure
difference between front and back
Turbulent
boundary
layer
Laminar
Flow
*
*

## Slide 33
IDEAL FLOW* LAMINAR  FLOW TURBULENT  FLOW
S e p a r a t i o n

## Slide 34
~82o
~120o
PRESSURE DRAG
DRAG
IF NO VISCOSITY
WHAT WOULD BE
TOTAL DRAG ?

## Slide 35
Smooth
Trip
By roughening surface
can “trip” boundary layer
so turbulent which results
in a favorable momentum
exchange, pushing
separation point further
downstream, resulting
in a smaller wake and
reduced drag.
125 yd drive with smooth
golf ball becomes 215 yds
for dimpled*
From Van Dyke, Album of Fluid Motion
Parabolic Press, 1982; Original photographs
By Werle, ONERA, 1980
Re = 15000
Re = 30000
Notes: SHAPE & FLOW
230 yards for dimples
50 yards for smooth

## Slide 36
Drag coefficient as a function of Reynolds number for smooth circular
cylinders and smooth spheres. From Munson, Young, & Okiishi,
Fundamentals of Fluid Mechanics, John Wiley & Sons, 1998
ASIDE: At low very low Reynolds numbers Drag  UL
CD = D / (1/2  U2Af)
D ~ U
CD = constant
D ~ U2

## Slide 37
Drag coefficient as a function of Reynolds number for smooth circular
cylinders and smooth spheres. From Munson, Young, & Okiishi,
Fundamentals of Fluid Mechanics, John Wiley & Sons, 1998
ASIDE: At low very low Reynolds numbers Drag  UL
CD = D / (1/2  U2Af)
D ~ U
CD = constant
D ~ U2

## Slide 38
Drag coefficient as a function of Re
for a smooth cylinder and smooth sphere.
ReDcrit ~ 3 x 105
3-D relieving effect
Cdcylinder>CDsphere
Is ReDcritical constant?

## Slide 39
Effect of surface roughness on the drag coefficient of a sphere in the
Reynolds number range where laminar boundary layer becomes turbulent.

## Slide 40: CD of Common Geometries

## Slide 41: CD of Common Geometries

## Slide 42: CD of Common Geometries